## Slide 1: CUDA Performance Considerations (2 of 2)
Varun Sampath
Original Slides by Patrick Cozzi
University of Pennsylvania
CIS 565 - Spring 2012

## Slide 2: Agenda
Instruction Optimizations
  Mixed Instruction Types
  Loop Unrolling
  Thread Granularity
Memory Optimizations
  Shared Memory Bank Conflicts
  Partition Camping
  Pinned Memory
Streams

## Slide 3: Mixed Instructions
Special Function Units (SFUs)
  Use to compute __sinf(), __expf()
  Only 4, each can execute 1 instruction per clock
Image: NVIDIA Fermi Whitepaper
Notes: 2 SFUs per SM on G80

## Slide 4: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Instructions per iteration
  One floating-point multiply
  One floating-point add
  What else?

## Slide 5: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Other instructions per iteration
  Update loop counter

## Slide 6: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Other instructions per iteration
  Update loop counter
  Branch

## Slide 7: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Other instructions per iteration
  Update loop counter
  Branch
  Address arithmetic

## Slide 8: Loop Unrolling
Instruction Mix
  2 floating-point arithmetic instructions
  1 loop branch instruction
  2 address arithmetic instructions
  1 loop counter increment instruction
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}

## Slide 9: Loop Unrolling
Only 1/3 are floating-point calculations
  But I want my full theoretical 1 TFLOP (Fermi)
  Consider loop unrolling
Image: NVIDIA Fermi Whitepaper

## Slide 10: Loop Unrolling
Pvalue +=
Ms[ty][0] * Ns[0][tx] +
Ms[ty][1] * Ns[1][tx] +
...
Ms[ty][15] * Ns[15][tx]; // BLOCK_SIZE = 16
No more loop
  No loop count update
  No branch
  Constant indices – no address arithmetic instructions
Notes: Compilers are getting better at unrolling, but many programmers still do it by hand.

## Slide 11: Loop Unrolling
Automatically:
#pragma unroll BLOCK_SIZE
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Under the hood: Predication
Disadvantages to unrolling?
Notes: Disadvantages include instruction cache misses and increased register usage. Manually unrolling avoids the disadvantages of predication (which itself is only used for a few-instruction branch).

## Slide 12: Aside: Loop Counters
for (i = 0; i < n; ++i)
{
out[i] = in[offset + stride*i];
}
Should i be signed or unsigned?
Notes: Undefined behavior in C can lead to some compiler optimizations. In this case, strength reduction can be used on stride*i because the compiler can do what it wants to if the multiplication overflows. Unsigned i would prevent this.

## Slide 13: Loop Unrolling Performance
Image from http://courses.engr.illinois.edu/ece498/al/textbook/Chapter5-CudaPerformance.pdf
Notes: The 1x1 versus 1x2 versus 1x4 is number of blocks merged, due to increased thread granularity. Next subject.

## Slide 14: Thread Granularity
How much work should one thread do?
  Parallel Reduction
    Reduce two elements?
  Matrix multiply
    Compute one element of Pd?
Notes: Adding some sequential-ness to our parallel implementations can actually improve performance.

## Slide 15
Slide from Vasily Volkov’s talk at SC11
Notes: Unroll the parallel loop is the important concept.

## Slide 16
Slide from Vasily Volkov’s talk at SC11

## Slide 17
Slide from Vasily Volkov’s talk at SC11

## Slide 18
Slide from Vasily Volkov’s talk at SC11

## Slide 19
Slide from Vasily Volkov’s talk at SC11

## Slide 20
Slide from Vasily Volkov’s talk at SC11
Notes: Also, more concurrent thread blocks get executed. Memory bound, not compute bound.

## Slide 21: All about Tradeoffs
Thread count
Block count
Register count
Shared memory size
Instruction size
Notes: Occupancy isn’t everything.

## Slide 22: Shared Memory
Fast pool of on-chip memory
Allocated per block
Note: runs at base clock instead of shader clock
Registers
Thread block slots
Thread slots
Shared memory
SM
8
768
8K registers
16K
G80 Limits
Shared memory access patterns can affect performance. Why?
Notes: Base clock source: http://www.beyond3d.com/content/reviews/55/7 and Vasily Volkov

## Slide 23: Bank Conflicts
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Shared Memory
  Sometimes called a parallel data cache
    Multiple threads can access shared memory at the same time
  Memory is divided into banks (Why?)
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0

## Slide 24: Bank Conflicts
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Banks
  Each bank can service one address per two cycles
  Per-bank bandwidth: 32-bits per two (shader clock) cycles
  Successive 32-bit words are assigned to successive banks
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0

## Slide 25: Bank Conflicts
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Bank Conflict: Two simultaneous accesses to the same bank, but not the same address
  Serialized
G80-GT200: 16 banks, with 8 SPs concurrently executing
Fermi: 32 banks, with 16 SPs concurrently executing
  What does this mean for conflicts?
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Notes: * 16 threads in a half-warp
Bank conflicts only occur within a half warp for G80, but within a full warp for Fermi

## Slide 26: Bank Conflicts
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Bank Conflicts?
  Linear addressing stride == 1
Bank Conflicts?
  Random 1:1 Permutation
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Notes: Neither of these have bank conflicts

## Slide 27: Bank Conflicts
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Bank Conflicts?
  Linear addressing stride == 2
Bank Conflicts?
  Linear addressing stride == 8
Thread 11
Thread 10
Thread 9
Thread 8
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 9
Bank 8
Bank 15
Bank 7
Bank 2
Bank 1
Bank 0
x8
x8
Notes: Left: 2-degree bank conflict
Right: 2-degree bank conflict

## Slide 28: Bank Conflicts
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Fast Path 1 (G80)
  All threads in a half-warp access different banks
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0

## Slide 29: Bank Conflicts
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Fast Path 2 (G80)
  All threads in a half-warp access the same address
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Same
address

## Slide 30: Bank Conflicts
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Slow Path (G80)
  Multiple threads in a half-warp access the same bank
  Access is serialized
  What is the cost?
Thread 11
Thread 10
Thread 9
Thread 8
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Notes: Cost: maximum number of simultaneous accesses to a single bank.
A degree-n bank conflict requires n times as many cycles to process as an access with no conflict.

## Slide 31: Bank Conflicts
__shared__ float shared[256];
// ...
float f = shared[index + s * threadIdx.x];
For what values of s is this conflict free?
  Hint: The G80 has 16 banks
Notes: “In this case, threads tid and tid+n access the same bank whenever s*n is a multiple of the number of banks (i.e. 32) or, equivalently, whenever n is a multiple of 32/d where d is the greatest common divisor of 32 and s. As a consequence, there will be no bank conflict only if the warp size (i.e. 32) is less than or equal to 32/d., that is only if d is equal to 1, i.e. s is odd. “ – CUDA Programming Guide

## Slide 32: Bank Conflicts
__shared__ float shared[256];
// ...
float f = shared[index + s * threadIdx.x];
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
s=1
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
s=3
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Notes: When s shares no common factors with the number of banks. s must be odd.
Another simple fix: __shared__ float tile[TILE_DIM][TILE_DIM+1]; // pad with one extra column  optimizing matrix transpose with CUDA source

## Slide 33: Bank Conflicts
Without using a profiler, how can we tell what kind of speedup we can expect by removing bank conflicts?
What happens if more than one thread in a warp writes to the same shared memory address (non-atomic instruction)?
Notes: * Change all shared memory reads to the same value: broadcast.
change shared memory reads to threadIdx.x: no conflicts.
* Only one thread per half-warp performs a write and which thread performs the final write is undefined

## Slide 34: Partition Camping
“Bank conflicts” of global memory
Global memory divided into 6 (G80) or 8 (GT200) 256-byte partitions
The 1 million KBps question: How do active half-warps in your kernel access memory?
Image: [Reutsch & Micikevicius, 2010]
Notes: Get it? Get it?

## Slide 35: Fixing Partition Camping
Diagonalize block indices
blockIdx_y=blockIdx.x;
blockIdx_x= (blockIdx.x+blockIdx.y)%gridDim.x;
Output:
Not a problem in Fermi (How?)
Image: [Reutsch & Micikevicius, 2010]
Notes: Fermi’s addresses are hashed.

## Slide 36: Page-Locked Host Memory
Page-locked Memory
  Host memory that is essentially removed from virtual memory
  Also called Pinned Memory

## Slide 37: Page-Locked Host Memory
Benefits
  Overlap kernel execution and data transfers
See G.1 in the NVIDIA CUDA C Programming Guide for full compute capability requirements
Time
Data Transfer
Kernel Execution
Data Transfer
Kernel Execution
Normally:
Paged-locked:

## Slide 38: Page-Locked Host Memory
Benefits
  Increased memory bandwidth for systems with a front-side bus
    Up to ~2x throughput
Image from http://arstechnica.com/hardware/news/2009/10/day-of-nvidia-chipset-reckoning-arrives.ars

## Slide 39: Page-Locked Host Memory
Benefits
  Option: Write-Combining Memory
    Disables page-locked memory’s default caching
    Allocate with cudaHostAllocWriteCombined to
      Avoid polluting L1 and L2 caches
      Avoid snooping transfers across PCIe
        Improve transfer performance up to 40% - in theory
    Reading from write-combining memory is slow!
      Only write to it from the host

## Slide 40: Page-Locked Host Memory
Benefits
  Paged-locked host memory can be mapped into the address space of the device on some systems
    What systems allow this?
    What does this eliminate?
    What applications does this enable?
  Call cudaGetDeviceProperties() and check canMapHostMemory
Notes: Hybrid CPU/GPU, mobile?, consoles
Eliminates the need to copy to and from host memory.
Enables applications where the memory transfer (bus bandwidth) was the bottleneck such as simple image processing.

## Slide 41: Page-Locked Host Memory
Usage:
cudaHostAlloc() / cudaMallocHost()
cudaHostFree()
cudaMemcpyAsync()
See 3.2.5 in the NVIDIA CUDA C Programming Guide
Notes: HostAlloc() allows flags, MallocHost() does not

## Slide 42: Page-Locked Host Memory
What’s the catch?
  Page-locked memory is scarce
    Allocations will start failing before allocation of in pageable memory
  Reduces amount of physical memory available to the OS for paging
    Allocating too much will hurt overall system performance

## Slide 43: Streams
Stream: Sequence of commands that execute in order
Streams may execute their commands out-of-order or concurrently with respect to other streams
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Stream A
Stream B

## Slide 44: Streams
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Stream A
Stream B
Time
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Is this a possible order?
Notes: Yes, synchronous in order

## Slide 45: Streams
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Stream A
Stream B
Time
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Is this a possible order?
Notes: Yes, synchronous in order

## Slide 46: Streams
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Stream A
Stream B
Time
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Is this a possible order?
Notes: Yes, interleaved

## Slide 47: Streams
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Stream A
Stream B
Time
Command 0
Command 2
Command 1
Command 0
Command 2
Command 1
Is this a possible order?
Notes: No, out of order within a stream

## Slide 48: Streams
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Stream A
Stream B
Time
Command 0
Command 1
Command 2
Command 0
Command 1
Command 2
Is this a possible order?
Notes: Yes, concurrent in order

## Slide 49: Streams
In CUDA, what commands go in a stream?
  Kernel launches
  Host device memory transfers

## Slide 50: Streams
Code Example
  Create two streams
  Each stream:
    Copy page-locked memory to device
    Launch kernel
    Copy memory back to host
  Destroy streams

## Slide 51: Stream Example (Step 1 of 3)
cudaStream_t stream[2];
for (int i = 0; i < 2; ++i)
{
cudaStreamCreate(&stream[i]);
}
float *hostPtr;
cudaMallocHost(&hostPtr, 2 * size);

## Slide 52: Stream Example (Step 1 of 3)
cudaStream_t stream[2];
for (int i = 0; i < 2; ++i)
{
cudaStreamCreate(&stream[i]);
}
float *hostPtr;
cudaMallocHost(&hostPtr, 2 * size);
Create two streams

## Slide 53: Stream Example (Step 1 of 3)
cudaStream_t stream[2];
for (int i = 0; i < 2; ++i)
{
cudaStreamCreate(&stream[i]);
}
float *hostPtr;
cudaMallocHost(&hostPtr, 2 * size);
Allocate two buffers in page-locked memory
Notes: Page-locked memory is required for streams to overlap

## Slide 54: Stream Example (Step 2 of 3)
for (int i = 0; i < 2; ++i)
{
cudaMemcpyAsync(/* ... */,
cudaMemcpyHostToDevice, stream[i]);
kernel<<<100, 512, 0, stream[i]>>>
(/* ... */);
cudaMemcpyAsync(/* ... */,
cudaMemcpyDeviceToHost, stream[i]);
}

## Slide 55: Stream Example (Step 2 of 3)
for (int i = 0; i < 2; ++i)
{
cudaMemcpyAsync(/* ... */,
cudaMemcpyHostToDevice, stream[i]);
kernel<<<100, 512, 0, stream[i]>>>
(/* ... */);
cudaMemcpyAsync(/* ... */,
cudaMemcpyDeviceToHost, stream[i]);
}
Commands are assigned to, and executed by streams

## Slide 56: Stream Example (Step 3 of 3)
for (int i = 0; i < 2; ++i)
{
// Blocks until commands complete
cudaStreamDestroy(stream[i]);
}

## Slide 57: Streams
Assume compute capabilities:
  Overlap of data transfer and kernel execution
  Concurrent kernel execution
  Concurrent data transfer
How can the streams overlap?
See F.1 in the NVIDIA CUDA C Programming Guide for more on compute capabilities

## Slide 58: Streams
Time
Kernel execution
Stream A
Stream B
Host device memory
Device to host memory
Kernel execution
Host device memory
Device to host memory
Can we have more overlap than this?

## Slide 59: Streams
Time
Kernel execution
Stream A
Stream B
Host device memory
Device to host memory
Kernel execution
Host device memory
Device to host memory
Can we have this?
Notes: Only Fermi supports concurrent kernel execution.

## Slide 60: Streams
Time
Kernel execution
Stream A
Stream B
Host device memory
Device to host memory
Kernel execution
Host device memory
Device to host memory
Can we have this?
Dependent on kernel completion
Blocked until kernel from Stream A completes

## Slide 61: Streams
Performance Advice
  Issue all independent commands before dependent ones
  Delay synchronization (implicit or explicit) as long as possible

## Slide 62: Streams
Rewrite this to allow concurrent kernel execution
for (int i = 0; i < 2; ++i)
{
cudaMemcpyAsync(/* ... */, stream[i]);
kernel<<< /*... */ stream[i]>>>();
cudaMemcpyAsync(/* ... */, stream[i]);
}

## Slide 63: Streams
for (int i = 0; i < 2; ++i) // to device
cudaMemcpyAsync(/* ... */, stream[i]);
for (int i = 0; i < 2; ++i)
kernel<<< /*... */ stream[i]>>>();
for (int i = 0; i < 2; ++i) // to host
cudaMemcpyAsync(/* ... */, stream[i]);
Notes: The copy from device to host that is dependent a kernel execution is now issued after both kernel launches

## Slide 64: Streams
Explicit Synchronization
  cudaThreadSynchronize()
    Blocks until commands in all streams finish
  cudaStreamSynchronize()
    Blocks until commands in a stream finish
See 3.2.5.5.3 in the NVIDIA CUDA C Programming Guide for more synchronization functions

## Slide 65: References
CUDA C Best Practices Guide, version 4.1
CUDA C Programming Guide, version 4.1
Reutsch, Greg and Micikevicius, Paulius. “Optimizing Matrix Transpose in CUDA.” June 2010.
Volkov, Vasily. “Unrolling parallel loops.” November 14, 2011. Slides

## Slide 66: Bibliography
Optimal Parallel Reduction Proof with Brent’s Theorem
Vasily Volkov. “Better Performance at Lower Occupancy.” Slides
Mark Harris. “Optimizing Parallel Reduction in CUDA.” Slides