## Slide 1: Mobile GPUs
Varun Sampath
University of Pennsylvania
CIS 565 - Spring 2012

## Slide 2: Agenda
SoCs
Case Studies
  NVIDIA Tegra 2, Tegra 3
  Imagination Technologies’ PowerVR SGX Series5XT
  Apple iPad (2012)
Future
Note about sources

## Slide 3: What is an SoC?
System-on-a-Chip
  CPU, GPU, DSP, I/O
  Single-chip solution
Top mobile SoC vendors:
  Qualcomm, Apple, TI, Samsung, NVIDIA
Advantages of using SoCs?
Disadvantages?
We will see all consumer chips converge to SoCs
Chart: Mobile SoC Market Share 2011
| Apple | NVIDIA | Qualcomm | Samsung | TI | Others
Marketshare 2011 | 22.7 | 3 | 31.4 | 13.8 | 17 | 12.1
Market Share Data from PC Perspective
Notes: Advantages:
Much lower energy (less off-chip interconnect)
Easier to build and mass-produce
Area savings
Disadvantages
Less flexibility with vendors
Stuck with components you may not need (IGPs for example)
Haswell will bring the I/O controller on-chip

## Slide 4: What is an SoC?
Image from iFixit
Notes: A5 has CPU, GPU, flash controller, even RAM in PoP design

## Slide 5: Block Diagram of TI OMAP 4470
Image from TI

## Slide 6: Brief Discussion of ARM
RISC CPU vendor that currently dominates mobile
Mobile Designs: Cortex-A8, A9, A15
Fabless Designer
  Core Design Licensees
  Architecture Licensees
    Qualcomm Scorpion/Krait
    NVIDIA

## Slide 7: The Constraints of Mobile
Energy
  Cell phone battery capacity of 5-7 Wh (tablets 20-40 Wh)
  How much energy can our chips consume?
Area
  PCB size constraints
  Cooling constraints
Notes: Must consider displays, radios. What are the dominant sources of battery drain?

## Slide 8: Some Energy Numbers
Data from AnandTech

## Slide 9: Some Contributors to Switching Energy
Off-chip Interconnect (to DRAM)
  Bandwidth is expensive
  Minimize reasons to fire up memory bus
High frequencies
  Requires increased voltages

## Slide 10: Some Theoretical Performance Numbers
 | Apple iPad 2 | ASUS Transformer Prime | Some Nice Desktop
CPU | A5 @ 1GHz | Tegra 3 @ 1.4GHz | Sandy Bridge @ 3.4GHz
GPU | POWERVR SGX543MP2 @ 250MHz | Mobile GeForce @ 500MHz | GTX680 @ 1GHz
Memory Interface | 64-bit @ (maybe) 800MHz = 6.4GB/s | 32-bit | 256-bit @ 6GHz = 192GB/s
GPU GFLOPS | 16 GFLOPS | 12 GFLOPS | 3 TFLOPS
Mobile Data from AnandTech
GTX680 Specs from Newegg

## Slide 11: GeForce GPU in NVIDIA Tegra 2
Image from NVIDIA
Notes: Note that mobile GeForce is a typical immediate mode renderer with early-z rejection.

## Slide 12: Tegra 2 Mobile GeForce
Separate vertex and pixel shaders
  4 of each, each capable of 1 multiply-add /clock
Pixel, texture, vertex, and attribute caches
  Reduce memory transactions
  Pixel cache useful for UI components
Memory controller optimizations
  Arbitrate between CPU & GPU requests
  Reorder requests to limit bank switching

## Slide 13: NVIDIA Tegra 3 (Kal-El)
Expanded Mobile GeForce
  4 vertex and 8 pixel shaders
4-PLUS-1 architecture
Image from AnandTech
Notes: Tegra 3 also has higher clocks for the GPU

## Slide 14: PowerVR SGX
TA (Tile Accelerator) – store scene data and split up screen into tiles
ISP (Image Synthesis Processor) – perform Hidden Surface Removal with z-testing
TSP (Texture and Shading Processor) – run pixel shader
Image from ImgTec

## Slide 15: PowerVR SGX Series5XT
Image from ImgTec
Notes: USSE2 unified shaders perform vertex and pixel shading. Multi-threaded execution units are 4-wide vector processors

## Slide 16: Summarizing PowerVR SGX Series5XT
Used in Apple A5, A5X
Unified shader architecture (called USSE2)
Tile based deferred rendering (TBDR)
  Will cover in more detail next week
Multi-core architecture

## Slide 17: Mobile GPU Families
Qualcomm Adreno
  Unified shaders, 4-wide SIMD
  immediate mode with early-z
Imagination Technologies’ PowerVR SGX Series5XT
  Unified shaders, 4-wide SIMD
  Tile based deferred rendering
NVIDIA Mobile GeForce
  Separate vertex (4) & pixel (8/12) shaders , scalar
  immediate mode with early-z
ARM Mali
  Separate vertex (1) & pixel (4) shaders , 4/2-wide SIMD
  immediate mode with early-z
Analysis by AnandTech

## Slide 18: Demands for Mobile
Higher screen resolutions
  Requires more memory bandwidth
  Pixel count growing higher than geometry?
Longer battery life
Higher quality mobile gaming

## Slide 19: Case Study: the new iPad
Screen resolution of 2048x1536
  Quadruple the pixels of previous 1024x768 version
  Higher than nearly all desktop and laptop displays
Battery life approximately equal to previous version
Gaming performance?

## Slide 20: iPad Gaming Performance
Image from AnandTech
Notes: Capped off by Vsync probably for 1024x768 case. Interesting note: Infinity Blade rendered at 1.4x of iPad 2 and then upscaled.

## Slide 21: Apple A5X Die Shot
Image from UBMTechInsights
Notes: Notice how much larger the GPU in total is than the CPU. Also notice how many DDR interfaces there are, and how they are surrounding the GPU.

## Slide 22: Apple iPad Statistics
 | Apple iPad 2 | Apple iPad (2012) | 11” Apple MBA
CPU | A5 @ 1GHz | A5X @ 1GHz | Sandy Bridge @ 1.8GHz
GPU | POWERVR SGX543MP2 @ 250MHz | POWERVR SGX543MP4 @ 250MHz | Sandy Bridge IGP @ 350MHz/1.2GHz
Memory Interface | 64-bit @ 800MHz = 6.4GB/s | 128-bit (for GPU) | 128-bit @ 1.3GHz = 20.8GB/s
Die Size | 122mm2 | 163mm2 | 149mm2
Battery Size | 25Wh | 42.5Wh | 35Wh
Data and Image from AnandTech

## Slide 23: What will the future bring?
GPU Compute
  PowerVR SGX Series5XT OpenCL capable, but no drivers
  Could do compute the old-fashioned way with GLSL
  Direct3D 11 means Compute Shader support
PowerVR Series6 press release suggests 100-1000 GFLOPS
Kepler-based GPU coming to a super phone near you?